## Slide 1: ANR & SWT & Reboot
MTK/周砾雄(Lixiong.Zhou@mediatek.com)

## Slide 2: Agenda
ANR
    ANR Knowledge Background
    ANR Checking SOP
    ANR Analysis Knowledge Base
    ANR Debug & Dump
    Case Share
  SWT
    Overview
    Watchdog’s Principle
    SWT Debug
    Case Share
  Reboot
    Categories
    Reason
    Debug

## Slide 3: ANR

## Slide 4: ANR knowledge background
What’s ANR?
ANR Type
ANR Generate Principle
How & What System(AMS) do when ANR
Proportion of bug and performance

## Slide 5: What’s ANR?
ANR stands for “Application Not Responding”
  ANR happens when an application’s UI thread blocks for a period of time.
  A dialog shows when ANR happens.
?
?
?

## Slide 6: ANR Generate Principle(1/3)
Long Time Execution
  Flow Break
System Server
App Process
Timeout
System Server
App Process
Timeout

## Slide 7: ANR Generate Principle(2/3)
SystemServer
Application
InputDispatcher
(touch/keyevent)
AMS
(broadcast/service bindcall)
MSG 1
MSG 2
MSG onClick
MSG onTouch
MSG onReceive
MSG onBind
MSG 3
MSG 4
MSG 5
Msg Queue
MainThread

## Slide 8: ANR Generate Principle(3/3)
SystemServer
Application
InputDispatcher
AMS
MSG 1
MSG 2
MSG onClick
MSG onTouch
MSG onReceive
MSG onBind
MSG 3
MSG 4
MSG 5
Msg Queue
Msg1 + msg2 exec too long  ANR
onClick/onTouch indeed
exec too long  ANR
As mentioned above
MainThread

## Slide 9: How & What System(AMS) do when ANR
AMS
Timeout of broadcast
Timeout executing service
Input dispatching timed out
appNotResponding()
APP MainThread
print event_log
print “ANR In” in log
dumpStackTraces()
create ANR.DB
show ANR Dialog
10s/60s
20s/200s
8s

## Slide 10: ANR Type(1/2)
Type | Function call | Log sample | Time out (s)
Input dispatch | onClick(),onTouch(),onKeydown(),onKeyup()…… | Input dispatching timed out | 8
Broadcast | onReceive() | Timeout of broadcast | FG: 10 BG 60
Service | onBind(),onCreate(),onStartCommand(),onUnbind(),onDestroy() | Timeout executing service | FG: 20 BG 200

## Slide 11: ANR Type(2/2)

## Slide 12
It took too long time deal with messages prior at these methods. But why?——> ANR Analysis
ANR occur，It might not really execute “onReceive()”, “onBind()”, “onTouch()” or other methods too long. However, at the mostly, it is because of “Main thread”：

## Slide 13: Proportion of bug and performance
Chart: 
| ANR Bug | ANR Performance
Status | 92 | 204

## Slide 14: Bug Issue & Performance Issue
ANR Bug | ANR performance
Dead Lock | IO wait high or heavy IO workload
Frequently message and last bound time | SQLite or wait lock
Stuck in binder server (not return) / driver | CPU occupied by other few process, CPU hotter(limit CPU core and frequency)
Memory leak | JE, NE, or other proc NE lead to
………… | …………

## Slide 15: ANR Checking SOP
Prepare
LOG
Check ANR Process
Check System Performance
Bug?

## Slide 16: Prepare LOG

## Slide 17: Prepare LOG

## Slide 18
SOP
SOP
SOP

## Slide 19: Steps Of Analyze ANR
Step 1: Confirm the time & pid of ANR from event log
Step 2:Check the call stack of main thread in ANR process
    Whether there are lots of message in message queue
    Whether it may perform a long time directly
    Check whether there is a lock synchronization
    Check whether it is performing binder communication, if so ,we should check the binder server
    Step 3: If can not get the root cause by above steps, it is may be a performance issue
Check Item | Log file
CPU loading | __exp_main.txt main_log
IO Wait | As above
CPU cores & CPU freqency | SYS_KERNEL_LOG
memory | sys_buddy_info/sys_memory_info

## Slide 20: ANR Analysis Knowledge Base
Search ANR pid & time
Search & Check Call Stack
Message History & Queue
CPU Usage
CPU Policy
Process Schedule Stats Information
Binder Info
Memory Info
Dexopt
Signal Processing
Check ANR Process
Check System Performance

## Slide 21: Check Main Thread State

## Slide 22: Search ANR pid & time
event_log/SYS_ANDROID_EVENT_LOG
main_log/sys_log/SYS_ANDROID_LOG
Suggested time period to check:
(anr_time - anr_timeout) ~ (anr_time + 2 secs)
10-14 16:19:12.661 822 845 E ANRManager: ANR in com.android.systemui, time=281371314
10-14 16:19:12.661 822 845 E ANRManager: Reason: Broadcast of Intent { act=android.intent.action.TIME_TICK flg=0x50000114 (has extras) }

## Slide 23: Check Main Thread Stack
In swt_jbt_trace file, we should locate the man thread at anr time point

## Slide 24: ThreadState(1/2)
Idle shows when the main thread’s message queue is not processing any message
Blocked shows this thread is blocked by another thread, so we should go on check other thread.

## Slide 25: ThreadState(2/2)
Waiting Or TimedWaiting shows this thread is waiting on Sb. to notify().We could find out it by call stack and “code”
Sleeping shows “main” is Sleeping due to call Sleep(ms).We need check out how long it will.

## Slide 26: Stuck in binder(1/2)
Following stacks means it is stuck in binder communication
But, following stacks don’t means it is stuck in binder

## Slide 27: Stuck in binder(2/2)
For server end following binder thread means it is idle
For server end following binder thread means it is busy now

## Slide 28: How To Analyze Binder Stuck Issue(1/3)
If we found main thread is stuck, we should confirm the server process first.
The most useful log is sys_binder_info file
Outgoing:meaning current thread is performing binder request to other process
Incoming: meaning current thread is performing binder service for other process
Clent end: pid and tid
sequence number in service file
Server end: pid and tid

## Slide 29: How To Analyze Binder Stuck Issue(2/3)
Step 1.Locate ANR pid & time
Step 2.Locate the call stack of the main thread

## Slide 30: How To Analyze Binder Stuck Issue(3/3)
Step 3.Check binder info to find out binder server
Step 4.Check process and thread,334:1005 map to /system/bin/mediaserver:Binder_1
Step 5:Check server end binder thread’s stack from swt_jbt_trace

## Slide 31: Message History & Queue(1/2)
When ANR occurs, AMS will dump last 20 message histories of main thread .(Just for eng or user debug version)
“__exp_main.txt” / main_log / sys_log.

## Slide 32: Message History & Queue(2/2)
Information of Message History
  Msg# :2 message serial number.
  Msg ID: 138
  Handler: target handler, to Handler (android.app.ActivityThread$H) followed by the callback (it might be null).
  Callback:null (it might be null), followed Handler
  Dispatching time: 2015-01-01 11:02:47.435 ,The time when the last message was dispatched.
  upTime: 2 ms,Total CPU execution time.
  elapsedTime: 2 ms, Total execution time including sleep time.
Msg#:2 <<<<< Finished to Handler (android.app.ActivityThread$H) {1162af80} null elapsedTime : 2 ms /upTime : 2 ms
Msg#:1 >>>>> Dispatching to Handler (android.app.ActivityThread$H) {1162af80} null: 138 from 2015-01-01 11:02:47.435

## Slide 33: Check CPU Loading, IOWait, Cores & Frequency ….

## Slide 34: CPU Information(1/2)
In kernel log we can get following information
1
2
3
4
5
6
1:current little online cpu numbers
2:current big online cpu numbers
3:current cpu loading
4:current io wait
5:little online cpu numbers after adjusting
6:big online cpu number after adjusting
So, If we found anr was not caused by thread block, we should check cpu information around anr period.

## Slide 35: CPU information(2/2)
Also can get CPU information from SYS_CPU_INFO
check the anr cpu usage
  In __exp_main.txt of anr db file
From this log, we can know the usage of CPU by every process

## Slide 36: CPU information
If cpu loading is too high(>80%?), we’d better to find which APP use too high and confirm whether it is normal
If io wait is too high(>50%?), we’d better first to check the I/O speed of flash.
If cpu core is less and frequency is slow, but cpu loading is higher, we should check the thermal issue

## Slide 37: Process Schedule Stats Information(1/N)
Check Process Schedule Stats Information between 2 timestamps
Time spent on the CPU
Time spent waiting on a run queue
# of time slices run on this CPU

## Slide 38: Process Schedule Stats Information(2/N)
Field 1 | Field 2 | Conclusion
Y | Y | It means the thread has been scheduled to run and has been waiting in the run queue
Y | N | It means this thread has been scheduled to run
N | Y | It means this thread has been waiting in the run queue but hasn’t been scheduled at all. In this case, we have to check FTRACE to find out who was occupying CPU.
N | N | It means the thread isn’t waiting for CPU scheduling. The process was either waiting for other thread to notify or it is really IDLE.
Inc ----> Y
Dec ----> N

## Slide 39: Process Schedule Stats Information(3/N)
librank was occupying CPU[2] in range of red circle

## Slide 40: Memory Info(1/2)
In sys_memory_info of db file, we can see the memory information
In SYS_BUDDY_INFO, we can see the use of physic memory
If the sum of Memfree and cached is small, there is memory issue
From this information we can see the fragment of physic memory
1
2
3
…
n
1: the number of 20 continuous pages
2:the number of 2n continuous pages
If there is only 20 continuous pages, the fragmentation is serious.

## Slide 41: Memory Info(2/2)
We also can get memory info from SYS_MEMORY_LOG, it record the memory change of a period of time including system memory and every process 'memory.
One process
One process
We should check which part or process use lots of memory , and analyze it as memory issue.

## Slide 42: CPU Policy
File : “kernel_log”
Keyword : “hps_main” and “cpufreq”

## Slide 43: Dexopt
File : main_log/sys_log
Keyword:
  ensurePackageDexOpt
  DexOpt: load 206ms, verify+opt 1492ms, 2050764 bytes
04-17 11:06:11.484 282 676 I ActivityManager: ensurePackageDexOpt too long duration ms: 1100
04-17 11:06:44.662 3200 3200 D dalvikvm: DexOpt: load 15ms, verify+opt 130ms
04-17 11:06:44.680 282 2254 I ActivityManager: ensurePackageDexOpt done duration ms: 336
Notes: http://online.mediatek.inc/_layouts/15/mol/topic/ext/Topic.aspx?mappingId=e6470a4e-6511-4391-8101-07629c14da39

## Slide 44: Signal Processing
Signal | Name | Description
3 | SIGQUIT | When ANR occurs, will send sig 3 to dump call stack.
9 | SIGKILL | Kill Process.
11 | SIGSEGV | When NE occurs will send sig 11.
18 | SIGTSTP | Restart process.
19 | SIGSTOP | Stop process.
Notice: Signal 3、19 will freeze process, so need to observe how long these signals make process freeze. If the time of process freezing is too long will lead to ANR or SWT.

## Slide 45
For bug, ANR process owner should fix it by themselves or other relative owner.
For performance, we should collect and analysis more information, such as CPU usage, memory info, binder info, IO wait and so on.

## Slide 46: ANR SOP(1/2)
Start
SYS_ANDROID_EVENT_LOG
Check ANR的时间点及进程的pid
SWT_JBT_TRACES
找到ANR该进程的backtrace
Check main thread
?
线程之间的held by是否形成一个环
Dead Locked
？
Y
Y
binder对端
对应的so
END
？
Y
Held by
N
Binder blocked
？
特殊Native call
？
CPU usage
优化CPU Usage过高的进程
END
Y
N
N
N

## Slide 47
ANR SOP(2/2)
Io wait
？
？
优化io过高的进程
END
Y
Y
CPU usage
N
优化CPU Usage过高的进程
？
Memory
？
优化memory过高的进程或者碎片
N
优化log打印
N
N
Log print
?
Y
Idle?
Message过多/执行时间长
Io call
？
？
优化Message
N
Y
？
No focus window
Check Activity状态是否为resume
END
Y
Y
N
N
N
Y
Y

## Slide 48: ANR debug & dump
For User/UserDebug：
  Dynamic adb shell command adb shell dumpsys activity log anr 2
  Modify code in AMS

## Slide 49: ANR debug & dump
 | USER/USERDEBUG | ENG
cpu usage | Y | Y
pre cpu usage | Y | Y
pre dump callstack | N | N
dump call stack | Y | Y
dump message history | N | Y
MTK dump stack trace for ANR at the default:

## Slide 50: Case Share

## Slide 51: SWT

## Slide 52: Why need SWT
System Server is a core process in Android system.
Some core services or looper threads run in it
  Once they are long time occupied, User experience will be very bad.
So, the watchdog mechanism is introduced to monitor the services or looper thread.
Once they are long time occupied, the android system will be restarted by watchdog.
System Server
Start Process
Privider Service
Manage Process
Secure Info
UI Input
Content Provider
Broadcast
………………

## Slide 53: How To Work
Watchdog Thread
Wait 30s
Check State
run
Check State is OK
If someone have waited over half of its setting time then dump all process’s back trace
OK
Over its setting time, then:
Dump All process’s back trace
Kill system server self
Check All Monitors registered before
Check Handlers added before
Just call monitor to try get lock, if long time can not get lock, may be hanged.
Just post to the front of its own looper thread, if not process by a long time, may be hang by the ahead of message

## Slide 54: Register To Be Monitored
If some services want to be monitored, it should be implements interface Monitor
  Then register it to Watchdog
If some looper thread want to be monitored, it is should be add Watchdog.
Such As:

## Slide 55: Check State
Every 30s, Watchdog thread will check all of their states
When check, Checker will post a message to the front of the looper.
When handle the message, it will check monitor and reset the state

## Slide 56: Services & Loopers

## Slide 57: Services & Loopers

## Slide 58: Services & Loopers

## Slide 59: Services & Loopers
Services
  All service’s lock time are 60s(except PackageManagerService:600s)
  Looper Thread
Looper thread | Default Time
PowerManagerService | 60s
PackageManagerService | 600s
ActivityManagerService | 60s
Main Thread | 60s
Ui Thread | 60s
Android.fg | 60s
i/o | 60s
Display Thread | 60s

## Slide 60: What to do when SWT happend
½ timeout
Pre dump system_server’s current back trace
Print in main log
**SWT happen **
Write to event log
Dump all java process’s back trace
Do sysRq(dump kernel back trace)
Kill system_server
timeout
We can get timepoint from event log

## Slide 61: How To Debug
Step 1. Confirm the time point
  From events log or SYS_ANDROID_EVENT_LOG
  Step 2. Check block thread or lock
  From SWT_JBT_TRACE
  Check the predump back trace
  Check the last back trace
  Check binder information
  Check lock state
  Check performance information
Watchdog Timepoint
Who block the watchdog

## Slide 62: Check predump call stacks
As mentioned before, at half of timeout, system_server’s all threads stack will be dumped.
So we should get the half timeout point first. Such as:
Then ,Check the block thread’s stack at half timeout point
Predump Time Point is:22:07:45 – 60/2s= 22:07:15

## Slide 63: Check last stacks
We also should check the last stack to confirm whether the thread really blocked or really run too long.

## Slide 64: Important information in stack
Tid:the sequence number of starting the thread in this process
sysTid: the thread id in system
State: current state of this thread in system
Schedstat:
      1: Time spent on the CPU
      2:Time spent waiting on a runqueue
      3: time slices run on this CPU
Check the differ of running time slices between predump and last stack, if there is a obviously difference, it’s meaning this stack run too long, else it’s meaning this thread is blocked or be suspended too long.
1
2
3

## Slide 65: Thread is blocked(1/2)
By Competition lock
1
1
Means tid = 75, so we should check the thread of tid=75 in this process
By Sleeping
We should check the stack to find the reason of sleep.

## Slide 66: Thread is blocked(2/2)
By waiting
Means: Object.wait() or Object.wait(n) is being called. So, we should check the source code first.

## Slide 67: Stuck in binder(1/2)
Following stacks means it is stuck in binder communication
But, following stacks don’t means it is stuck in binder

## Slide 68: Stuck in binder(2/2)
For server end following binder thread means it is idle
For server end following binder thread means it is busy now

## Slide 69: How To Analyze Binder Stuck Issue(1/3)
If we found main thread is stuck, we should confirm the server process first.
The most useful log is sys_binder_info file
Outgoing: meaning current thread is performing binder request to other process
Incoming: meaning current thread is performing binder service for other process
Clent end: pid and tid
sequence number in service file
Server end: pid and tid

## Slide 70: How To Analyze Binder Stuck Issue(2/3)
Step 1.Locate ANR pid & time
Step 2.Locate the call stack of the main thread

## Slide 71: How To Analyze Binder Stuck Issue(3/3)
Step 3.Check binder info to find out binder server
Step 4.Check process and thread,334:1005 map to /system/bin/mediaserver:Binder_1
Step 5:Check server end binder thread’s stack from swt_jbt_trace

## Slide 72: Performance

## Slide 73: CPU Information(1/2)
In kernel log we can get following information
1
2
3
4
5
6
1:current little online cpu numbers
2:current big online cpu numbers
3:current cpu loading
4:current io wait
5:little online cpu numbers after adjusting
6:big online cpu number after adjusting
So, If we found swt was not caused by thread block, we should check cpu information around swt period.

## Slide 74: CPU information(2/2)
Get CPU information from SYS_CPU_INFO
Some time before SWT, may some ANR of app happened, so we can check the anr around the SWT.
  In __exp_main.txt of anr’s db file
From this log, we can know the usage of CPU by every process

## Slide 75: CPU information
If cpu loading is too high(>80%?), we’d better to find which APP use too high and confirm whether it is normal
If io wait is too high(>50%?), we’d better first to check the I/O speed of flash.
If cpu core is less and frequency is slow, but cpu loading is higher, we should check the thermal issue

## Slide 76: Memory Info(1/2)
In sys_memory_info of db file, we can see the memory information
In SYS_BUDDY_INFO, we can see the use of physic memory
If the sum of Memfree and cached is small, there is memory issue
From this information we can see the fragment of physic memory
1
2
3
…
n
1: the number of 20 continuous pages
2:the number of 2n continuous pages
If there is only 20 continuous pages, the fragmentation is serious.

## Slide 77: Memory Info(2/2)
We also can get memory info from SYS_MEMORY_LOG, it record the memory change of a period of time including system memory and every process 'memory.
One process
One process
We should check which part or process use lots of memory , and analyze it as memory issue.

## Slide 78: Case Share

## Slide 79: Case 1
CRID: ALPS02848434
Analyse:
1. get time point of SWT in sys_android_event_log
2.Check predump stack

## Slide 80: Case 1
3.Check last stack
We can see there is no change between predump and last stack. So we can sure that this thread is blocked. And blocked by wait. From the wifi knowledge we should check the WifiStateMachine thread. And we’d better let the owner of wifi go on analyze this issue.

## Slide 81: Case 2
CRID:ALPS02758402
Analyze:
  1. get time point and blocked thread
  2. Check predump stack

## Slide 82: Case 2
  3. Check last stack
  We can see it, this thread is not fully blocked. So we should to confirm what has done by this thread.
  Then check main log

## Slide 83: Case 2
  We found following information from main log
  That’s meaning it takes a too long time to dex2oat,so we should let it do quickly.
  Then we finally give a patch to customer.

## Slide 84: Case 3
CRID:ALPS02578376
Analyse:
  1. get time point and blocked thread
  2.Check predump stack

## Slide 85: Case 3
  3. Check last stack
  We can see that it is blocked by Mediaplayer

## Slide 86: Case 3
  According the code of MediaPlayer, we know the function of prepare will perform a binder communication with mediaserver asynchronously and will be notify by mediaserver also with binder communication. But we check sys_binder_info, we found all of binder thread in system_system are occupied.
  If all binder thread are occupied, the new binder request will not be processed, so the android.ui thread can not be notified. Then cause SWT.

## Slide 87: Case 3
As mentioned before, if all binder threads are occupied, the new binder request can not be processed, including someone publish provider. So from now on ,there is no anybody can have binder communication with system_server.

## Slide 88: Case 4
CRID:ALPS02947564
Analyse:
  Get time point and pid
  Check predump stack
Cmd line: system_server
"android.fg" prio=5 tid=14 Blocked
| group="main" sCount=1 dsCount=0 obj=0x12cd0c10 self=0xa9187e00
| sysTid=942 nice=0 cgrp=default sched=0/0 handle=0xa085a930
| state=S schedstat=( 892620493 1166957552 1861 ) utm=51 stm=38 core=0 HZ=100
| stack=0xa0758000-0xa075a000 stackSize=1038KB
| held mutexes=
at com.android.server.am.ActivityManagerService.monitor(ActivityManagerService.java:21166)
- waiting to lock <0x03abc805> (a com.android.server.am.ActivityManagerService) held by thread 88
at com.android.server.Watchdog$HandlerChecker.run(Watchdog.java:200)
at android.os.Handler.handleCallback(Handler.java:815)
at android.os.Handler.dispatchMessage(Handler.java:104)
at android.os.Looper.loop(Looper.java:207)
at android.os.HandlerThread.run(HandlerThread.java:61)
at com.android.server.ServiceThread.run(ServiceThread.java:46)

## Slide 89: Case 4
  Check thread of hold the lock
  Check last stack
    Actually, from the two stack, we can fount that there is a dead lock.
  Solution
    Just check stack and try to find why, and then resolve it.
  Notice
    It is danger to modify the code of framework, especially those run in System_server
"Binder_B" prio=5 tid=88 Blocked
| group="main" sCount=1 dsCount=0 obj=0x135d10a0 self=0x99173e00
| sysTid=2876 nice=0 cgrp=default sched=0/0 handle=0x9777a930
| state=S schedstat=( 6306323924 4301998027 11509 ) utm=433 stm=197 core=3 HZ=100
| stack=0x9767e000-0x97680000 stackSize=1014KB
| held mutexes=
at android.app.ActivityThread.acquireExistingProvider(ActivityThread.java:5137)
- waiting to lock <0x0fffa826> (a android.util.ArrayMap) held by thread 11
at android.app.ActivityThread.acquireProvider(ActivityThread.java:5017)
at android.app.ContextImpl$ApplicationContentResolver.acquireUnstableProvider(ContextImpl.java:2023)
at android.content.ContentResolver.acquireUnstableProvider(ContentResolver.java:1517)
at android.content.ContentResolver.query(ContentResolver.java:482)
at android.content.ContentResolver.query(ContentResolver.java:441)

## Slide 90: Useful tool
Tool name:E-Consulter
Download:
Use eservice count login and download

## Slide 91: How to use
Login---Use esevice count and password
Select the phenomenon of you concern, if swt ,you can select reboot.
Then all this category of issue will be list

## Slide 92: Read report
Then click right button to analyze detail

## Slide 93: Reboot

## Slide 94: OverView
We can let the mobile be in the initial state by performing reboot.
So there are normal reboot and abnormal reboot.
Normal Reboot
  Reboot system by the reboot flow
  Such as :Long press power button
  Abnormal Reboot
    May some exceptions happened in core processes or kernel or hardware.
    May hang detected in system or kernel

## Slide 95: How to check normal reboot
If reboot system, we always call shutdown thread, so in system_log, we can find following logs:
Or in last_kmsg
[ 358.968339] (0)[1:init]Reboot Process(adbd:377).
[ 360.033989] (0)[1:init]reboot: Restarting system with command ''
[ 360.034334] -(0)[1:init][<ffffffc0000becf4>] SyS_reboot+0x19c/0x1f0

## Slide 96: How to check Whether reboot
Always ,If normal reboot, we can not see the change of system_server’s pid in events log. Logs as following, 969 is system_server’s pid
Abnormal reboot
  Java Exception in Zygote or System_server
  Native Exception in Zygote ,System server, surfaceflinger or other core process
  Trigger watchdog in system_server(SWT)
  Kernel Exception
    Kernel Panic
    Thremal Reboot
    Hardware Reboot
    Hang detectet
    …….
    For abnormal reboot
      If exception happened, just analyze exception
      But for Watchdog, we should check lots of logs